## Slide 1: Rich Code For Tiny Computers
A Simple Commodore 64 Game in C++17
http://tinyurl.com/RichCodeCppCon2016

## Slide 2: Poll – I regularly program for:
Desktop / server / embedded CPUs like ARM and x86
Microcontrollers
40 year old 8 bit CPUs

## Slide 3: The Plan
Implement a simple game for the Commodore 64
In C++17
Have fun while doing it

## Slide 4: The Tools
Matt Godbolt’s Compiler Explorer @mattgodbolt
  http://gcc.godbolt.org
clang git build for C++17 features
x86-to-6502 conversion tool (more on that in a minute)

## Slide 5: The Why
I grew up using the Commodore 64
But never really had an understanding of its architecture
I recently decided to learn more and wanted to use my favorite programming language…
But no modern compilers officially supported 40 year old 6502 CPU…

## Slide 6: The How
We’ll use a modern C++ compiler with full optimizations to generate very simple x86 code
Then translate this to 6502 code for the C64
Most people consider this to be insane, but it turns out it was easier than actually trying to support 6502 with llvm
Besides, doing the crazy thing is more fun (when not being paid to do it)

## Slide 7: x86-to-6502
main:
movb $10, %al
.LBB0_1:
movb %al, 53280
movzbl 53280, %eax
incb %al
jmp .LBB0_1
main
lda #10
sta $03
lbb01
lda $03
sta 53280
sta $03
inc $03
jmp lbb01

## Slide 8
https://en.wikipedia.org/wiki/Commodore_64#/media/File:Commodore-64-Computer.png

## Slide 9: Then Vs Now
Commodore 64
$595 ($1481 in today’s dollars)
1.023Mhz 6502 (NTSC)
64kB RAM
8 bit CPU with 16 bit address space
Acer Aspire One 11
$150 (~1/10 the price)
Dual Core Celeron 1.6-2.5Ghz (4880x)
2GB RAM (32768x)
64 bit CPU
Our demo today can easily fit in the L1 cache of this CPU

## Slide 10: Then Vs Now
Commodore 64
$595 ($1481 in today’s dollars)
1.023Mhz 6502 (NTSC)
64kB RAM
8 bit CPU with 16 bit address space
MSP430-FR5849
$5.53 (Less in bulk)
16 Mhz
66kB RAM
16 bit CPU
Some level of official gcc and clang support today.

## Slide 11: The Game

## Slide 12: Simple pong clone
7
3
Ball
Paddles
Scores
Bouncy Walls

## Slide 13: 30 second computer architecture intro
Oversimplified, incomplete, and likely to get lots of comments on YouTube about what I left out.

## Slide 20
Example: Video Chip
In C64: The VIC-II

## Slide 21
CPU
RAM
VICII

## Slide 22: The overhead game
Some Overhead?
No overhead?

## Slide 23: Memory mapped hardware

## Slide 24: Memory mapping
Devices are connected directly to the CPU’s address bus
Reading and writing to specific memory locations controls devices
Example: setting 0xD020 = 1 tells the video controller to set the border color to white.

## Slide 26: Video Memory

## Slide 27
Background: Address 53281 0xD021
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | … | 33 | 34 | 35 | 36 | 37 | 38 | 39
40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | … | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | … | 113 | 114 | 115 | 116 | 117 | 118 | 119
880 | 881 | 882 | 883 | 884 | 885 | 886 | 887 | … | 913 | 914 | 915 | 916 | 917 | 918 | 919
920 | 921 | 922 | 923 | 924 | 925 | 926 | 927 | … | 953 | 954 | 955 | 956 | 957 | 958 | 959
960 | 961 | 962 | 963 | 964 | 965 | 966 | 967 | … | 993 | 994 | 995 | 996 | 997 | 998 | 999
Border: Address 53280 0xD020
Body: Default Address 1024 0x0400
.
.
.

## Slide 29: Dealing with colors

## Slide 30: The ViC-II Supports 16 Colors
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

## Slide 31: The ViC-II Supports 16 Colors
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
“Red” RGB(136, 57, 50)
“Light Red” RGB(184, 105, 98)

## Slide 32: Working with a fixed palette
Goal: easier working with the C64’s fixed palette
Idea: converting from RGB to the nearest available color
How: pretend that RGB values represent X,Y,Z coordinates in 3D space, look for the closest points
Note: this is not accurate to how the human eye sees colors, but it works for this purpose

## Slide 34: Daily programming puzzle

## Slide 35: Constexpr palette work
What we did here works because the compiler is able to optimize it
The programming puzzle for today is to make the nearest_color<> template fully constexpr enabled
If you succeed, there’s a following puzzle to sort the palette by luma, at compile-time with constexpr

## Slide 36: Using C++14
This problem will actually be much easier once C++17 is fully available
Today, however, we have C++14
This exercise will help you appreciate how more constexpr support in the standard library can help you make more efficient code

## Slide 37: joystick

## Slide 38: joysticks
2 Joystick Ports
State of joystick is accessed via the memory map

## Slide 39: joysticks
Port B – Joystick #1 – 56321 (0xDC01) |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  | ! Fire | ! Right | ! Left | ! Down | ! Up
Port A – Joystick #2 – 56320 (0xDC00) |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  | ! Fire | ! Right | ! Left | ! Down | ! Up

## Slide 41: RAII

## Slide 42: RAII
Resource Acquisition Is Initialization
Essentially – using constructors and destructors to manage state and resources
Many consider this to be the greatest strength of C++
I like to put this another way: well-defined object lifetime is C++’s greatest strength

## Slide 44: Commodore 64 Sprites

## Slide 45: Vic-II sprites
8 hardware sprites
Hardware sprite collision detection
Sprites are 24x21 pixels
Sprites can be single color or multicolor
Sprites can have their height or width doubled

## Slide 46: Monochrome sprite
Each bit represents 1 pixel

## Slide 49
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 50
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
126
30
120

## Slide 51
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 126 | 0
1 | 255 | 128
7 | 255 | 224
15 | 255 | 240
15 | 255 | 240
30 | 126 | 120
30 | 126 | 120
62 | 126 | 124
63 | 255 | 252
63 | 255 | 252
63 | 255 | 252
63 | 255 | 252
63 | 255 | 252
19 | 255 | 200
27 | 255 | 216
13 | 255 | 176
14 | 126 | 112
7 | 129 | 224
1 | 255 | 128
0 | 126 | 0
0 | 0 | 0

## Slide 53: Cppcast T-shirt

## Slide 54: Multi color sprite
Every 2 bits represents 2 pixels of the same color.

## Slide 57
0 | 0 | 1 | 1
3 | 1 | 1 | 3
1 | 1 | 0 | 0

## Slide 58
0 | 0 | 1 | 1
3 | 1 | 1 | 3
1 | 1 | 0 | 0
00 | 00 | 01 | 01
11 | 01 | 01 | 11
01 | 01 | 00 | 00

## Slide 59
0 | 0 | 1 | 1
3 | 1 | 1 | 3
1 | 1 | 0 | 0
00 | 00 | 01 | 01
11 | 01 | 01 | 11
01 | 01 | 00 | 00
5
215
80

## Slide 60
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 3 | 1 | 1 | 3 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 3 | 1 | 1 | 3 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 2 | 1 | 1 | 1 | 1 | 2 | 1 | 0 | 0
0 | 0 | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 2 | 2 | 2 | 2 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 61
00 | 00 | 00 | 00 | 01 | 01 | 01 | 01 | 00 | 00 | 00 | 00
00 | 00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00 | 00
00 | 00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00 | 00
00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00
00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00
00 | 00 | 01 | 01 | 11 | 01 | 01 | 11 | 01 | 01 | 00 | 00
00 | 01 | 01 | 01 | 11 | 01 | 01 | 11 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00
00 | 00 | 01 | 10 | 01 | 01 | 01 | 01 | 10 | 01 | 00 | 00
00 | 00 | 01 | 01 | 10 | 01 | 01 | 10 | 01 | 01 | 00 | 00
00 | 00 | 00 | 01 | 10 | 10 | 10 | 10 | 01 | 00 | 00 | 00
00 | 00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00 | 00
00 | 00 | 00 | 00 | 01 | 01 | 01 | 01 | 00 | 00 | 00 | 00
00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0 | 85 | 0
1 | 85 | 64
1 | 85 | 64
5 | 85 | 80
5 | 85 | 80
5 | 215 | 80
21 | 215 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
5 | 85 | 80
6 | 85 | 144
5 | 150 | 80
1 | 170 | 64
1 | 85 | 64
0 | 85 | 0
0 | 0 | 0

## Slide 63: Putting It All together

## Slide 64
320
200

## Slide 65
255
200

## Slide 67: Wrap-up

## Slide 68: Why does this work?
Straightforward logic
Very little branching
Letting the compiler work for us
  Function inlining is very important
  Compile-time calculations save runtime work
How much RAM did we use at runtime?

## Slide 69: Zero overhead abstractions
Objects
Methods
(Delegating) Constructors / Destructors
Lambdas with/without capture
Structured bindings (aka destructuring)
Function calls that have been inlined
Templates

## Slide 70: Questions
CppCast (http://cppcast.com)
C++ Weekly YouTube Channel
http://articles.emptycrate.com/idocpp
Learning C++ Best Practices
Inheritance and Polymorphism with C++