## Slide 1: Rich Code For Tiny Computers
A Simple Commodore 64 Game in C++17

## Slide 2
Who here regularly needs to write software for 40 year old 8 bit CPUs?
What about modern small micro controllers?
Maybe efficient software for desktop and embedded platforms?

## Slide 3: The Plan
Implement a simple game for the Commodore 64
In C++17
Have fun while doing it

## Slide 4: The Tools
Matt Godbolt’s Compiler Explorer @mattgodbolt
  http://gcc.godbolt.org
clang git build for C++17 features
x86-to-6502 conversion tool

## Slide 5: The Why
The Commodore 64 was first sold in 1982 but still has an active culture of users and programmers
If we can convince our modern compiler to generate code a 34 year old computer can run…
Then we can write better code for our modern computers

## Slide 6: Then Vs Now
Commodore 64
$595 ($1481 in today’s dollars)
1.023Mhz 6502
64kB RAM
8 bit CPU with 16 bit address space
Acer Aspire One 11
$150 (~1/10 the price)
Dual Core Celeron 1.6-2.5Ghz (4880x)
2GB RAM (32768x)
64 bit CPU
Our demo today can easily fit in the L1 cache of this CPU

## Slide 7: Then Vs Now
Commodore 64
$595 ($1481 in today’s dollars)
1.023Mhz 6502
64kB RAM
8 bit CPU with 16 bit address space
MSP430-FR5849
$5.53 (Less in bulk)
16 Mhz
66kB RAM
16 bit CPU
Some level of official gcc and clang support today.

## Slide 8: The Game

## Slide 9: Simple pong clone
7
3
Ball
Paddles
Scores
Bouncy Walls

## Slide 10: 30 second computer architecture intro
Oversimplified, incomplete, and likely to get lots of comments on YouTube about what I left out.

## Slide 17
Example: Video Chip
In C64: The VIC-II

## Slide 18: Memory mapped hardware

## Slide 19: Memory mapping
Devices are connected directly to the CPU’s address bus
Reading and writing to specific memory locations controls devices
Example: setting 0xD020 = 1 tells the video controller to set the border color to white.

## Slide 21: Video Memory

## Slide 22
Background: Address 53281 0xD021
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | … | 33 | 34 | 35 | 36 | 37 | 38 | 39
40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | … | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | … | 113 | 114 | 115 | 116 | 117 | 118 | 119
840 | 841 | 842 | 843 | 844 | 845 | 846 | 847 | … | 873 | 874 | 875 | 876 | 877 | 878 | 879
880 | 881 | 882 | 883 | 884 | 885 | 886 | 887 | … | 913 | 914 | 915 | 916 | 917 | 918 | 919
920 | 921 | 922 | 923 | 924 | 925 | 926 | 927 | … | 953 | 954 | 955 | 956 | 957 | 958 | 959
Border: Address 53280 0xD020
Body: Default Address 1024 0x0400
.
.
.

## Slide 24: Dealing with colors

## Slide 25: The ViC-II Supports 16 Colors
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

## Slide 26: The ViC-II Supports 16 Colors
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
“Red” RGB(136, 57, 50)
“Light Red” RGB(184, 105, 98)

## Slide 27: Working with a fixed palette
Goal: easier working with the C64’s fixed palette
Idea: converting from RGB to the nearest available color
How: pretend that RGB values represent X,Y,Z coordinates in 3D space, look for the closest points
Note: this is not accurate to how the human eye sees colors, but it works for this purpose

## Slide 29: Daily programming puzzle

## Slide 30: Constexpr palette work
What we did here works because the compiler is able to optimize it
The programming puzzle for today is to make the nearest_color<> template fully constexpr enabled
If you succeed, there’s a following puzzle to sort the palette by luma, at compile-time with constexpr

## Slide 31: joystick

## Slide 32: joysticks
2 Joystick Ports
State of joystick is accessed via the memory map

## Slide 33: joysticks
Port B – Joystick #1 – 56321 (0xDC01) |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  | ! Fire | ! Right | ! Left | ! Down | ! Up
Port A – Joystick #2 – 56320 (0xDC00) |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  | ! Fire | ! Right | ! Left | ! Down | ! Up

## Slide 35: RAII

## Slide 36: RAII
Resource Acquisition Is Initialization
Essentially – using constructors and destructors to manage state and resources
Sometimes considered to have “too much overhead…”

## Slide 38: Commodore 64 Sprites

## Slide 39: Vic-II sprites
8 hardware sprites
Hardware sprite collision detection
Sprites are 24x21 pixels
Sprites can be single color or multicolor
Sprites can have their height or width doubled

## Slide 40: Monochrome sprite
Each bit represents 1 pixel

## Slide 43
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 44
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
126
30
120

## Slide 45
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 126 | 0
1 | 255 | 128
7 | 255 | 224
15 | 255 | 240
15 | 255 | 240
30 | 126 | 120
30 | 126 | 120
62 | 126 | 124
63 | 255 | 252
63 | 255 | 252
63 | 255 | 252
63 | 255 | 252
63 | 255 | 252
19 | 255 | 200
27 | 255 | 216
13 | 255 | 176
14 | 126 | 112
7 | 129 | 224
1 | 255 | 128
0 | 126 | 0
0 | 0 | 0

## Slide 47: Multi color sprite
Every 2 bits represents 2 pixels of the same color.

## Slide 50
0 | 0 | 1 | 1
3 | 1 | 1 | 3
1 | 1 | 0 | 0

## Slide 51
0 | 0 | 1 | 1
3 | 1 | 1 | 3
1 | 1 | 0 | 0
00 | 00 | 01 | 01
11 | 01 | 01 | 11
01 | 01 | 00 | 00

## Slide 52
0 | 0 | 1 | 1
3 | 1 | 1 | 3
1 | 1 | 0 | 0
00 | 00 | 01 | 01
11 | 01 | 01 | 11
01 | 01 | 00 | 00
5
215
80

## Slide 53
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 3 | 1 | 1 | 3 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 3 | 1 | 1 | 3 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 2 | 1 | 1 | 1 | 1 | 2 | 1 | 0 | 0
0 | 0 | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 1 | 0 | 0
0 | 0 | 0 | 1 | 2 | 2 | 2 | 2 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 54
00 | 00 | 00 | 00 | 01 | 01 | 01 | 01 | 00 | 00 | 00 | 00
00 | 00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00 | 00
00 | 00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00 | 00
00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00
00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00
00 | 00 | 01 | 01 | 11 | 01 | 01 | 11 | 01 | 01 | 00 | 00
00 | 01 | 01 | 01 | 11 | 01 | 01 | 11 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00
00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00
00 | 00 | 01 | 10 | 01 | 01 | 01 | 01 | 10 | 01 | 00 | 00
00 | 00 | 01 | 01 | 10 | 01 | 01 | 10 | 01 | 01 | 00 | 00
00 | 00 | 00 | 01 | 10 | 10 | 10 | 10 | 01 | 00 | 00 | 00
00 | 00 | 00 | 01 | 01 | 01 | 01 | 01 | 01 | 00 | 00 | 00
00 | 00 | 00 | 00 | 01 | 01 | 01 | 01 | 00 | 00 | 00 | 00
00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0 | 85 | 0
1 | 85 | 64
1 | 85 | 64
5 | 85 | 80
5 | 85 | 80
5 | 215 | 80
21 | 215 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
21 | 85 | 84
5 | 85 | 80
6 | 85 | 144
5 | 150 | 80
1 | 170 | 64
1 | 85 | 64
0 | 85 | 0
0 | 0 | 0

## Slide 56: Putting It All together

## Slide 58: Wrap-up

## Slide 59: Why does this work?
Straightforward logic
Very little branching
Letting the compiler work for us
  Function inlining is very important
  Compile-time calculations save runtime work
How much RAM did we use at runtime?

## Slide 60: Questions?

## Slide 61
CppCast (http://cppcast.com)
C++ Weekly YouTube Channel
http://articles.emptycrate.com/idocpp
Learning C++ Best Practices
Inheritance and Polymorphism with C++